## Slide 1
P.I.N.G
Private, decentralized communication on Raspberry Pi Pico 2
PHASE 1 · TEXT MESSAGING
Raspberry Pi Pico 2 · MicroPython · nRF24L01+ · 2.4 GHz

## Slide 2
Team
Project contributors
Members
Kelvin S. A. — Roll No. 17
Kabilan M. — Roll No. 20
S. Mukesh — Roll No. 33

## Slide 3
Why P.I.N.G?
A radio mesh that does not depend on the internet
Motivation
No central servers or commercial providers
Low-cost hardware: Pico 2 + nRF24L01+
Mesh by design: one shared address and channel
Built to grow: text today, voice and services later
What ships in Phase 1
Text messages over 2.4 GHz
128×64 SSD1306 OLED display
USB serial console input/output
Pure-Python protocol, covered by host tests

## Slide 4
Hardware
Bill of materials and radio wiring
Bill of materials
Raspberry Pi Pico 2 (RP2350)
nRF24L01+ radio module, SPI, 3.3 V only
0.96" SSD1306 OLED, 128×64, I2C
~10 µF decoupling capacitor on radio power
Breadboard and jumper wires
Radio wiring (SPI0)
MISO → GP16 • CSN → GP13
SCK → GP18 • MOSI → GP19
CE → GP14 • IRQ → GP21 (reserved)
OLED (I2C0): SDA → GP4, SCL → GP5
Address 0x3C, 400 kHz

## Slide 5
Repository layout
MicroPython firmware plus a pure-Python protocol
Project structure
firmware/pico/boot.py, main.py — entry points
firmware/pico/ping/ — application modules (protocol, radio, display, console)
firmware/pico/lib/ — vendored nrf24l01.py and ssd1306.py
firmware/pico/config.py — pins, RF channel/address, NODE_ID
firmware/pico/tests/ — on-device bring-up scripts
tests/ — host-side pytest suite • docs/ — hardware, protocol, roadmap

## Slide 6
Wire protocol
Every packet is exactly 32 bytes
32
bytes per packet
nRF24 payload size
Offset | Size | Field | Notes
0 | 1 | version | currently 1
1 | 1 | type | TEXT / ACK / BEACON / AUDIO
2 | 1 | src | sender node ID
3 | 1 | dst | recipient, 0xFF = broadcast
4 | 2 | seq | little-endian sequence number
6 | 1 | flags | reserved
7 | 1 | length | payload length, max 24
8 | 24 | payload | UTF-8 text, zero padded

## Slide 7
How a node runs
Main loop at a glance
1
Read line
Poll USB console for input
2
Parse
Text broadcasts, @id directs
3
Send
Build packet, radio.send()
4
Poll RX
nRF24 status register
5
Dedupe
Track (src, seq) pairs
6
Display
OLED and console output

## Slide 8
Roadmap
Phase 1 is complete; Phase 2 and 3 are planned
Phase 1 (current)
MicroPython on Pico 2
Text over nRF24L01+
SSD1306 OLED + serial console
Polled RX, shared address
Phase 2 (voice calls)
Gateway board (BLE/Wi-Fi)
Interrupt-driven RX (IRQ on GP21)
AUDIO packets, codec, jitter buffer
Half-duplex push-to-talk
Phase 3 (host servers)
Tiny HTTP server on gateway
Status page on the LAN
Post messages into the mesh
Richer routing and discovery
Phase 1 ships today; later phases build on the same protocol and hardware foundation.

## Slide 9
Deployment and dev workflow
From host to many boards
Getting running
Set a unique NODE_ID per board; keep radio settings identical
Deploy: mpremote fs cp boot.py, main.py, ping/, lib/
With multiple boards attached, prefix commands with a port (mpremote devs)
Host tests: python -m pytest
Format and lint: ruff format . then ruff check .

## Slide 10
Summary
Low-cost hardware forms a private mesh network
Clear separation: protocol, radio, display, console
Phase 1 delivers working text messaging now
Designed to grow into voice (Phase 2) and self-hosted services (Phase 3)
Phase 1 ships today